5.1 HUAWEI NGN reports

5.1.1 Traffic Congestion Statistics [/Shared Reports/Global Traffic Statistics]

Soft Switch Report CSV Files: TKGRP INCOMING OFFICE TRAFFIC, TKGRP OUTGOING OFFICE TRAFFIC, M3UA Signaling link traffic, CPU Seizure Ratio Traffic, Destination TRAFFIC Comments: (.CSV TASK FILE AVAILABLE AND PROVIDED TO BOCO) Report Format:

| Softx | Date Hour | Signaling Link Congestion Times | Signaling Links Congestion Duration | Local Switch Congestion Duration | Lost Call due to Internal Congestion |
| --- | --- | --- | --- | --- | --- |
| 2008-4-30 9:00 |
| 2008-4-30 10:00 |
| …… |
| Total |

Continued

| Trunk Circuit Congestion duration | Lost Calls due to Circuit GRP Congestion Times | Lost Calls due to Peer end congestion | CPU Congestion times | CPU Congestion Duration (Sec) |
| --- | --- | --- | --- | --- |

Formulae:

| Report Parameter | Formula | Remarks |
| --- | --- | --- |
| Softx | Soft switch Name & IP mapping to be provided | mapping to be provided |
| Date Hour |
| Signaling Link Congestion Times | SUM(TSCON) | M3UA Signaling link traffic |
| Signaling Links Congestion Duration | SUM(DSCON) | M3UA Signaling link traffic |
| Local Switch Congestion Duration | SUM(CGT) | TKGRP INCOMING OFFICE TRAFFIC |
| Lost Call due to Internal Congestion | SUM(INTCGCL) | TKGRP INCOMING OFFICE TRAFFIC |
| Trunk Circuit Congestion duration | SUM(CGT) | TKGRP OUTGOING OFFICE TRAFFIC |
| Lost Calls due to Circuit GRP Congestion Times | SUM(CGCCL) | Destination TRAFFIC |
| Lost Calls due to Peer end congestion | SUM(TIPEFCCG) -> TOPEFCCG | TKGRP OUTGOING OFFICE TRAFFIC |
| CPU Congestion times | SUM(CG) | CPU Seizure Ratio Traffic |
| CPU Congestion Duration (Sec) | SUM(CGT) | CPU Seizure Ratio Traffic |

Note:

- 1. Select a Date range, select multi hours, multiple soft switches;

- 2. This is an hourly report;

5.1.4 Trunk Group Statistic (OG) (/Shared report/Office Direction Traffic)

Soft Switch Report CSV Files: TKGRP OUTGOING OFFICE TRAFFIC Comments: (.CSV TASK FILE AVAILABLE AND PROVIDED TO BOCO) Report Format

| Softx | Office Direction | Trunk Group | start time | Installed Circuit Number | Avail Circuit Number | Blocked Circuit Number |
| --- | --- | --- | --- | --- | --- | --- |

(Continued)

| Circuit Avail Ratio (%) | Call Attempt Times | Seizure Times | Connected Times | Answer Times | Seizure Traffic (ERL) | Connected Traffic (ERL) | Answer Traffic (ERL) | Answer Attempt Ratio (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

(Continued)

| Overflow Times | Answer Seizure Ratio (%) | Traffic per line (ERL) | Abandon After Ring Times | No Answer Times | User Busy Times | Average Seizure Duration (SEC) | Congestion duration | Congestion times (peer end) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Formulae:

| Report Parameter | Formula | remarks |
| --- | --- | --- |
| Softx | Look up by Device IP |
| Office Direction | From Manual Configuration(to be provided by PTCL) |
| Trunk Group | Measuring Object |
| Start Time |
| Installed Circuit Number | INSBICIR |
| Avail Circuit Number | AVABICIR |
| Blocked Circuit Number | BLKBICIR |
| Circuit Avail Ratio | (AVABICIR / INSBICIR)*100% |
| Call Attempt Times | BID |
| Seizure Times | SEIZ |
| Connected Times | CNT |
| Answer Times | ANS |
| Seizure Traffic | SERL |
| Connected Traffic | CERL |
| Answer Traffic | RERL |
| Answer Attempt Ratio | (ANS / BID)*100% |
| Answer Seizure Ratio | (ANS / SEIZ)*100% |
| Traffic per line | SERL/ INSBICIR |
| Abandon After Ring Times | ARGABN |
| No Answer Times | LTNANS |
| User Busy Times | CBSY |
| Average Seizure Duration | AST |
| Overflow Times | OFL |
| Congestion duration | CGT |
| Congestion times (peer end) | POFCCG |

Note:

- 1. Select a Date range, select multi hours, and multiple soft switches.

- 2. Need a web page to edit office direction for each TG.

- 3. Add a busy hour report: based on seizure traffic. TG level. Can select a date range. Yesterday by default.

5.1.5 Trunk group statistics (IC) [/Shared Reports/Office Direction Traffic]

Soft Switch Report CSV Files: TKGRP INCOMING OFFICE TRAFFIC Comments: (.CSV TASK FILES AVAILABLE AND PROVIDED TO BOCO) Report Format

| Softx | Office Direction | Trunk Group | Start time | Installed Circuits | Avail Circuits | Blocked Circuits | Seizure Times | Connected Times | Answer Times | Seizure Traffic (ERL) | Connected Traffic (ERL) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

(Continued)

| Answer Traffic (ERL) | Answer Seizure Ratio (%) | Traffic per line (ERL) | Abandon After Ring Times | No Answer Times | User Busy Times | Average Seizure Duration (SEC) | Congestion Duration | Lost Call Internal Congestion Times | Congestion times (peer end) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Formulae:

| Report Parameter | Formula | remarks |
| --- | --- | --- |
| Softx Name | Look up by Device |
| Office Direction | From Manual Configuration(to be provided by PTCL) |
| Trunk Group | Measuring Object |
| Start Time |
| Installed Both way Circuit Num | INSBICIR |
| Avail Both way Circuit Num | AVABICIR |
| Blocked Bi-Directional Circuit Num | BLKBICIR |
| Seizure Times | SEIZ |
| Call Connected Times | CNT |
| Answer Times | ANS |
| Seizure Traffic | SERL |
| Connected Traffic | CERL |
| Answer Traffic | RERL |
| Answer Seizure Ratio | (ANS / SEIZ)*100% |
| Traffic per line | SERL / INSBICIR |
| Abandon After Ring Times | ARGABN |
| Ringed No Answer Times | LTNANS |
| Called Busy Times | CBSY |
| Average Seizure Duration | AST |
| Congestion Duration | CGT |
| Lost Call Internal Congestion Times | INTCGCL |
| Congestion times (peer end) | TIPEFCCG |

Note:

- 1. Select a Date range, select multi hours, and multiple soft switches.

- 2. Select a softswitch and provide option for choosing particular Office Direction and Trunk group

- 3. Add a busy hour report: based on seizure traffic. TG level. Can select a date range. Yesterday by default.

5.1.6 Trunk Group statistics (IC + OG) [/Shared Reports/Office Direction Traffic]

Soft Switch Report CSV Files: TKGRP OUTGOING OFFICE TRAFFIC, TKGRP INCOMING OFFICE TRAFFIC Comments: (.CSV TASK FILE AVAILABLE AND PROVIDED TO BOCO) Report Format

| Softx | Office Direction | Trunk Group | start time | Installed Circuits | Avail Circuits | Blocked Circuits |
| --- | --- | --- | --- | --- | --- | --- |

(Continued)

| Seizure Times | Connected Times | Answer Times | Seizure Traffic (ERL) | Connected Traffic (ERL) | Answer Traffic (ERL) |
| --- | --- | --- | --- | --- | --- |

(Continued)

| ASR_IC (%) | ASR_OG (%) | Traffic per line (ERL) | Abandon After Ring Times | No Answer Times | User Busy Times | Average Seizure Duration (SEC) |
| --- | --- | --- | --- | --- | --- | --- |

(Continued)

| CFR | NER | MHT | MCT | Call Rate | Justified Circuit |
| --- | --- | --- | --- | --- | --- |

Formulae:

| Report Parameter | Formula | remarks |
| --- | --- | --- |
| Softx | Device |
| Office Direction | From configuration data |
| Trunk Group | Measuring Object |
| Start Time |
| Installed Circuits | INSBICIR | From TKGRP OUTGOING OFFICE TRAFFIC |
| Avail Circuits | AVABICIR | From TKGRP OUTGOING OFFICE TRAFFIC |
| Blocked Circuits | BLKBICIR | From TKGRP OUTGOING OFFICE TRAFFIC |
| Seizure Times | SEIZ (IC + OG) |
| Connected Times | CNT (IC + OG) |
| Invalid address times | IADDT(IC) |
| Answer Times | ANS (IC + OG) |
| Seizure Traffic | SERL (IC + OG) |
| Empty code times | EMPTY(IC+OG) |
| Connected Traffic | CERL (IC + OG) |
| Answer Traffic | RERL (IC + OG) |
| ASR_IC | (ANS / SEIZ)*100% for IC |
| ASR_OG | (ANS / SEIZ)*100% for OG |
| Traffic per line | SERL(IC+OG) / INSBICIR | INSBICIR From TKGRP OUTGOING OFFICE TRAFFIC |
| Abandon After Ring Times | ARGABN (IC + OG) |
| Ringed No Answer Times | LTNANS (IC + OG) |
| User Busy Times | CBSY (IC + OG) |
| INCOMPLETE DIALLING TIMES | INCOM(IC+OG) |
| CALLED BUSY TIMES | CBSY (IC+OG) |
| CFR | from PTCL later |

| NER | (ANS + EMPTY + IADDT + INCOM + ARGABN (IC+OG) + CBSY + LTNANS) / SEIZ |
| --- | --- |
| MHT | ((I.SEIZURE TRAFFIC + O.SEIZURE TRAFFIC) / (I.SEIZURE TIMES + O.SEIZURE TIMES)) *3600 |
| MCT | ((I.ANSWER TRAFFIC + O.ANSWER TRAFFIC) / (I.ANSWER TIMES + O.ANSWER TIMES)) *3600 |
| Call Rate | Connected Times / 3600 (IC + OG) |
| Justified Circuits | Based on Erlang B table | Erlang B table provided earlier will still hold good |

Note:

- 1. Select a Date range, select multi hours, multiple soft switches.